# Vapor Recovery Certification Procedure

###### CP - 201

###### Certification Procedure for

###### Vapor Recovery Systems at

Gasoline Dispensing Facilities

Adopted:  December 9, 1975

Amended:  March 30, 1976

Amended:  August 9, 1978

Amended:  December 4, 1981

Amended:  September 1, 1982

Amended:  April 12, 1996

Amended:  April 28, 2000

Amended:  February 1, 2001

Amended:  June 1, 2001

Amended:  July 25, 2001

Amended:  July 3, 2002

Amended:  March 7, 2003

Amended:  July 1, 2003

Amended:  October 8, 2003

Amended:  August 6, 2004

Amended:  February 9, 2005

Note:   The only portion of this procedure being amended is section 2, which includes Table 2-1 and the addition of section 2.4.5, the balance of the text remains as amended on August 6, 2004. The text is shown in strikeout to indicate text that is proposed for deletion and underline to indicate text that is proposed for additions.

Table 2-1

Effective and Operative Dates for Performance Standards and Specifications

| Performance Type | Requirement | Sec. | Effective Date | Operative Date |
| --- | --- | --- | --- | --- |
| All Phase I Standards and Specifications | As specified in Table 3-1 | 3 | April 1, 2001 | July 1, 2001 |
| ORVR Compatibility for GDF > 2.0 million gal/yr throughput | As specified in section 2.4.5 and section 4.4 Interaction When Refueling ORVR Vehicles Shall Meet the applicable Efficiency or Emission Standard, Including ORVR Penetrations to 80% | 4.1, 4.4 | September 1, 2001 April 1, 2001 | April 1, 2003 |
| ORVR Compatibility for GDF ≥ 1.0 million gal/yr throughput1 | As specified in section 2.4.5 and section 4.4 | 4.4 | January 1, 2002 | April 1, 2003 |
| ORVR Compatibility for GDF < 1.0 million gal/yr throughput1 | As specified in section 2.4.5 and section 4.4 | 4.4 | March 1, 2002 | April 1, 2003 |
| Nozzle Criteria | Post-Refueling Drips ( 3 drop/refueling | 4.7 | January 1, 2005 April 1,2004 | January 1, 2005 April 1,2004 |
| Liquid Retention | ( 350 ml/1,000 gals. | 4.8 | April 1, 2001 | July 1, 2001 |
| Liquid Retention Nozzle Spitting | ( 100 ml/1,000 gals. ( 1.0 ml /nozzle/fueling | 4.8 | January 1, 2005 April 1,2004 | January 1, 2005 April 1,2004 |
| Spillage (including drips from spout) | ( 0.24 pounds/1,000 gallons | 4.3 | January 1, 2005 April 1,2004 | January 1, 2005 April 1,2004 |
| For GDF > 1.8 mil. gal/yr. | ISD Requirements | 10 | April 1, 2005 April 1,2004 | April 1, 2005 April 1,2004 |
| For GDF > 600,000 gal/yr. | ISD Requirements | 10.1 | April 1, 2006 April 1,2005 | April 1,2006 April 1, 2005 |
| Unihose | One Hose/Nozzle per Dispenser Side | 4.11 | Not applicable | April 1, 2003 |
| All other Phase II Standards and Specifications | As specified in Tables 4-1 through 8-2. | 4,5,6, 7,8 | January 1, 2005 April 1,2004 | January 1, 2005 April 1,2004 |

Add new section 2.4.5 to section 2.4:

2.4.5	The gasoline dispensing facility’s gasoline throughput for calendar year 2003 shall be used for determining compliance with the Onboard Refueling Vapor Recovery (ORVR) requirements in Table 2-1.

# Footnotes

Effective January 1, 2001, state law requires the certification of only those systems that are ORVR compatible (Health and Safety Code section 41954, as amended by Chapter 729, Statutes of 2000; Senate Bill 1300).

GDF ≤ 600,000 gal/yr are exempted from ISD requirements.