# Vapor Recovery Certification Procedure

###### CP - 201

###### Certification Procedure for

###### Vapor Recovery Systems at

Gasoline Dispensing Facilities

Adopted:  December 9, 1975

Amended:  March 30, 1976

Amended:  August 9, 1978

Amended:  December 4, 1981

Amended:  September 1, 1982

Amended:  April 12, 1996

Amended:  April 28, 2000

Amended:  February 1, 2001

Amended:  June 1, 2001

Amended:  July 25, 2001

Amended:  July 3, 2002

Amended:  March 7, 2003

Amended:  July 1, 2003

##### Amended:  October 8, 2003

Amended: ________________

Note: The text is shown in strike-out to indicate text that is proposed for deletion and underline to indicate text that is proposed for addition. Only the amended section is shown.

4.11		Unihose MPD Configuration

There shall be only one hose and nozzle for dispensing gasoline on each side of a multi-product dispenser (MPD).  This shall not apply to facilities installed prior to April 1, 2003 unless the facility replaces more than 50 percent of the dispensers or makes a modification, other than the installation of required sensors, that modifies over 50 percent of the vapor piping in the dispensers.  Facility modifications that meet the definition of “major modification” for a Phase II system in D-200 trigger the unihose requirement as the facility is considered a “new installation”.  Exception: dispensers which must be replaced due to damage resulting from an accident or vandalism may be replaced with the previously installed type of dispenser.